Course:	03.451		Forest Science I

Unit 7:	Fire and the Forest

Lesson 4:	Uses of Prescribed Burning

GPS:	AG-FS-5-D

Academic Standard:……………………………………………. ELA9LSV1, ELA9LSV2, SCSh2, SCSh9

Objective:

List uses of prescribed fire.

Teaching Time:

1 hour

References:

International Paper School Forest Lesson Guide.

A Guide for Prescribed Fire in Southern Forests. Technical Publication R8-TP11

Georgia Forest Landowner Manual Cooperative Extension Service. University of Georgia. Athens, GA.

Forest and Forestry, Interstate Publishers,

Inc.  Danville IL.

http://www.gfc.state.ga.us

Materials and Equipment:

Video tape “Prescribed Burning” (available from an area forestry teacher)

Video tape “The two sides of Fire”

Teaching Procedure

Introduction and Mental Set

View video tape Prescribed Burning.

Discussion

1.	If a wildfire can cause damage to our forest, how would a fire be used for good?  List on board: Go over reasons for prescribed burning.

(a) Hazard Reduction -- Hazard reduction is the reduction and control 	of forest litter and undergrowth. Georgia has some 11,000 forest 	fires per year that burn more than 50,000 acres. Areas that have 	been prescribed burned every few years generally are immune to 	wildfire damage. Hazard reduction or fuel management is even 	more important in pine plantations because of the high investment 	required to establish them. Many plantations can be prescribed 	burned once they reach approximately 15 feet average height.

(b) Hardwood Control -- Hardwood and brush species, unlike pines, do 	not need open area or full sunlight to live they can invade southern 	pine forests. This unwanted growth prevents successful pine 	regeneration and even competes with large pines for nutrients and 	moisture. By using prescribed burns over a period of time most of 	the hardwoods 2" in diameter or under can be controlled. One or 	more of these burns should be a summer burn to get the best 	results.

(c) Site Preparation -- In order to establish pines, bare soil and full 	sunlight is needed. Fire is the most economical tool that can be 	used to help provide these conditions. To establish a stand 	naturally a program of several prescribed burns is usually needed 	prior to harvest. This can reduce hardwood shade and competition 	and provide a suitable seedbed. We can greatly reduce the cost of 	mechanical or chemical site preparation when it is preceded by 	prescribed burning.

(d) Wildlife Habitat -- Wildlife habitat can be greatly improved by 	prescribed burning. The burn reduces predator cover, exposes 	hidden seeds and increases herb and legumes as well as 	producing fresh low browse. The proper size, frequency and 	season of burns, as well as other factors, are important in 	managing wildlife habitat.

(e) Disease Control -- Prescribed burning is the only practical method of   	controlling Brown Spot Needle Blight. Generally, a later winter burn 	is recommended when 25% of seedlings two years or older are 	infected. The fire burns away the infected needles without killing the 	well protected bud.

Reduction of litter in pine plantations also seems to reduce the 	incident of Fomes Annosus Root Rot. This disease is often found in 	winter thinned plantations growing on sandy soils. There is no 	known control for this disease once it gets established. However 	prescribed burning and thinning during the worm months of the 	year seem to reduce the occurrence of this deadly disease.

(f) Improved Accessibility -- Reducing the ground cover by prescribed 	burning improves accessibility and visibility for marking and cruising 	timber harvesting operations and other management and marketing 	activities. It can also improve recreational and aesthetic values and 	provide better access for hunters or bird watchers.

2.	What is prescription burning?

A.	The application of fire to the land to accomplish specific silvicultural, wildlife, grazing, or fire hazard reduction purposes.

B.	The most economical tool to use for cleaning operations in young pine stands.

C.	Under ideal conditions, fire can be used for less that $3 per acre.

D.	Prescription burning should be only done by persons trained in its use.

E.	Before using prescription burning, the use needs to measure:

(1)  relative humidity

(2)  temperature

(3)  wind, velocity and direction

(4)  fuel moisture

Summary

Prescribed burning in our forest is a very good management tool used by foresters to achieve various management objectives.

Evaluation

Review reasons for prescription burning and have students give them orally.

End of unit written evaluation at end of unit 7.