Course:  Landscape Design and Management

Unit 4: Establishing a Hardscape

Pretest and Post test

- A patio with a wooden surface raised above ground level is called?

a.	walk				b.	retaining wall

c.	drive				d.	deck

- The physical features of a landscape such as fences, walks, or pools are called?

a.	hardscape			b.	softscape

c.	bookscape			d.	poolscape

- What is the percent slope of an area that drops five vertical feet for every 100 horizontal feet?

a.	2				b.	3

c.	4				d.	5

- Main walkways should be at least _______ feet wide.

a.	1				b.	2

c.	3				d.	4

- What are three walkway construction materials?

- What are three retaining wall construction materials?

- What is the term for boards that provide support for the decking boards?

a.	joist				b.	beam

c.	footing			d.	ledger board

- Calculate the size of a pool liner using the following formula.

length of pool + (2 x depth of pool) + 2’ = length of liner

width of pool + (2 x depth of pool) + 2’ = width of liner

The pool is 10’ long, 8’wide, and 2’ deep.

- Calculate the amount of 4” x 8” brick pavers needed for a patio measures 8’ x 16’.

- Calculate the amount of mulch needed for a 4’ x 25’ walkway.  The mulch depth is three inches.

Area Formula:	length x width

Volume

Formula:	area (in square feet) x depth (in inches)  = cubic feet

12

cubic feet  =  cubic yard

27

11 – 20.	Identify hand and power tools used with the installation of hardscapes.