Course:	03.431		Aquaculture

Unit 11:		Aquatic Structures and Equipment

Lesson 1:		Aquaculture Ponds

QCC:

Objectives:

In Aquaculture:

1. Distinguish between four types of ponds.

2. Identify factors in pond site selection.

3. Explain important pond construction requirements.

4. Identify site-specific factors that determine costs.

5. List factors to consider when planning pond size.

6. Identify layout and design considerations.

7. List advantages of small versus large ponds.

In Science:

1. Identify species for pond, cage, raceway, tank or silo culture.

2. List steps in determining a site’s water quality.

3. Determine whether soil is suitable for pond construction.

Teaching Time:

Teaching Time:

Laboratory Time:

Materials and Equipment:

DVD player

Projector

Computer

PowerPoint Presentations

References:

Parker, Rick, Aquaculture Science, Delmar Publishers, Inc. Albany, NY.

Teaching Procedure

Discussion

Ponds and raceways are the most common structures for raising fish.

Procedure

Ponds – Four types of ponds are natural, impoundment, excavated and 			levee.  Harvest techniques depend on the size of the animals, the 			intensity of production, and the species cultured. (Table 11-1 Fish 			Pond Types, P. 379)

Design Standards and Construction – Methods of harvest and fish 				requirements determine the size and depth of the pond.  Multiple 			ponds should be constructed where they can be drained and filled 			separately.

Size – Fish ponds range for .1 to 20 acres.  Pond size is determined by site 		conditions, construction equipment, and harvest methods.  Site and 		design are very important to profitability.

Water Supplies – Watershed ponds are filled by runoff, but can be supplied 		by groundwater, and surface water.  Water containing wild fish should 		be filtered.

Soil Characteristics – Dams should be built using at least 20% clay.  Soil 			should be sampled frequently during dam construction.  (Figure 11-3, 		p. 381)

Topography – Topography affects the size and shape of a watershed pond.  		Steep slopes in valleys require dams of larger volume per water 			surface acre than sites with gently sloping hills.  Therefore they cost 		more to produce.  Watershed ponds should be less than 10 feet deep 		at the drain.

Other Considerations – During pond site selection, the site should be an 			area where the pipes and valves can be installed to drain the pond 			completely.  The shorelines should be at least 3 feet deep.  Pond 			bottoms should be smooth and slope gently to the drainpipe.  			Flooding from rivers should not be allowed to flow into the ponds.

Cost of Construction – Cost estimates should include clearing, earth fill, 			excavation, pipe and drain, concrete, seeding, and road gravel.

Site Selection of Levee-Type Production Ponds – Construction costs, ease  		and cost of operation, and productivity can affect each site selected.

Water Availability

Water Sources

Soil Characteristics

Topography

Wetlands

Draining

Flooding

Utility Right-of-Ways

Pesticides

Summary

Evaluation

Written test