## Slide 1: How to Lay Out a Sqare

## Slide 2: Gather Supplies
Tools
Measuring Tape – Long enough to measure diagonal lines of your shape
Hammer
Square
Level (if needed)
Materials
Nails (large enough?) 80d (80 penny) has an 8” shank
Builder’s string
Flag stakes (optional)

## Slide 3: Step 1 – Establish a Base Line (First Side)
28’ or 336”
Pretty simple. Place one nail, measure distance, place second nail, and tie your string in between.
This is your base line. Once you are satisfied with your measurement and location, this line will NEVER move.
For our example, we will lay out the 1st “box” for the HS Lawnmower CDE Course.

## Slide 4: Step 2 – Square a Perpendicular Line
28’ or 336”
28’ 10 9/16”
7’ 1” or 85”
Lay out your 2nd line perpendicular and square with the 1st. A diagonal measurement
Can be calculated using the Pythagorean Theorum

## Slide 5: Step 3 – 3rd Line Parallel to the 1st Line
28’ or 336”
28’ 10 9/16”
7’ 1” or 85”
Lay out your 3rd line parallel with and the same length as the 1st.
28’ or 336”

## Slide 6: Step 4 – 4th Line Parallel to the 2nd Line
28’ or 336”
28’ 10 9/16”
7’ 1” or 85”
Lay out your 4th line parallel with and the same length as the 2nd.
28’ or 336”
7’ 1” or 85”

## Slide 7: Step 5 – Check Diagonal Measurements
28’ or 336”
28’ 10 9/16”
7’ 1” or 85”
Your Diagonal Measurements should be identical if square.
28’ or 336”
7’ 1” or 85”

## Slide 8: Final Product
28’ or 336”
7’ 1” or 85”
Box 1 Complete!
28’ or 336”
7’ 1” or 85”